## Slide 1: Greenpeace visit to the Priargunskiy uranium works
Krasnokamensk, Russian Federation, 1994
Presentation for the safeND Uranium Mining Workshop

## Slide 2
1994 Greenpeace Sweden visited Krasnokamensk region (eastern Siberia)
Purpose - investigate and document reported environmental and health problems associated with uranium mining and refining at the Priargunskiy Uranium Works
Part of a larger campaign to investigate environmental problems associated with the Swedish nuclear fuel cycle

## Slide 3: Reason for choosing Priargunskiy
In 1994:
–Approximately 40% of all uranium imported into Sweden comes from the former Soviet Union (Swedish nuclear inspectorate SKI)
–All of U exported to Sweden from RF originates in RF enrichment centers (Albert Shishkin, General Manager TECHSNABEXPORT, monopolist for U export from RF)
–All uranium used as feedstock in enrichment facilities originates in Russia (Albert Shishkin)
--Priarguskiy Uranium Works is the only functioning uranium mine in RF

## Slide 4: Priargusky Uranium Works
-Largest uranium mine in the world (1994)
-Only active uranium works in RF (1994)
-Uranium deposits discovered in 1964
-Produced 40% of Soviet uranium
-Originally for military purposes
-1994 – 100% for export

## Slide 5: Priargusky Uranium Works
Consists of (1994):
--3 underground uranium mining complexes
--1 open pit uranium mine
--1 open pit coal quarry
--One 500 Mw coal power plant
--Ore processing plant (RPK)
--Chemical refining plant (GMZ)
--Sulphuric acid production plant (SKZ)
--Machinery manufacturing and refit base (RMZ)
-

## Slide 6: Production process:
1. Uranium ore is removed from the mines or open pit.
2. The ore is graded by concentration of U235.
3. Sufficiently high grade ore is taken to the Central Ore Yard for storage. Lower grade ore is dumped into "empty” ore piles.
4. Ore from the Central Ore Yard is transported to the RPK.

## Slide 7: Production process:
5. At RPK the ore is milled and washed. The resulting fine grained powder is transported to the GMZ. Liquid waste into tailing ponds
6. At GMZ the ore undergoes a series of chemical processes, which yields U3O8 in powder form. The purity of the product is up to 99%. The level of enrichment of U235 is 0.71%(natural). Liquid waste into tailing ponds.
7. The U3O8 is packaged and shipped to foreign customers or enrichment plants.

## Slide 8: Reported health concerns
In 1993 a report was published by the East Siberian Section of the Siberian Division of the Russian Academy of Medical Sciences in Irkutsk, entitled:
Preliminary Medical and Ecological Expertise of Certain Population Centers of the Chita Region
The report was based on a visit to the area by the Academy’s researchers as well as an analysis of medical records.

## Slide 9: Report findings:
p. 91 "Of particular concern is the increase of the proportion of tumours as the cause of death among males which over the studied period has increased sharply by 3.2 times. If 1979 they held the last place in the structure of death rate of the male population, by 1991 they were already in third place.”

## Slide 10: Report findings:
p.124 “in the city of Krasnokamensk is registered a negative tendency of an increase in the cases of newly discovered neoplasm of digestive organs by 1.9 % of respiratory systems by 9.0 %, and lymphatic and blood creating systems by 30.9 %.”

## Slide 11: Report findings:
p.137 “In the city of Krasnokamensk is noted an increase of cancer rates, especially of the blood system”

## Slide 12: Report conclusions:
pp 232-240
“Thus, as follows from the data received as a result of the study, the environmental-hygienic situation which has formed on the studied territories of the cities of Baley and Krasnokamensk can be considered critical....
In the living quarters of the city of Krasnokamensk -- village of Oktyabrskiy, as a result of uranium and molybdenum ore mining and processing activities of the Priargunskiy Mining Chemical Combine… there has appeared an extremely unfavourable radiation situation, connected to technogenic uranium contamination (maximal values are 380 time greater than background, while in the drinking water of kindergartens and other communal water sources preliminary measurements showed values which exceed it by 1000 times) and a high degree of radon and its daughter products in living and office spaces in concentrations comparable to the maximal permitted levels…”

## Slide 13: Report conclusions:
CONT:
“The materials received are sufficient for making administrative decisions for stopping communal construction, on the territory of the village, and including the inhabitants of this zone into the list of people with the right of compensation analogous to Chernobyl zone, as well as early pensions.”

## Slide 14: Open pit uranium mine:
–Uranium ore dust clouds
–Transport by open truck
–insufficient PPM for
workers

## Slide 15: Underground mine
–Uranium dust and radon
–Contaminated water and air
pumped to the surface
–insufficient PPM for workers

## Slide 16: Ore storage yard
-Open area, ca 200 by 100 m
-Numerous uncovered piles of
uranium ore up to 5m height
-Constantly dusty due to
loading and offloading trucks,
-Situated on an exposed hill top
buffeted by winds.
-Source of stolen construction material
-As a result, the dust is spread out to a large area.settling on roads, fields, pastures and village streets. Spread further by trucks.

## Slide 17: Chemical processing plant
-Large volumes of liquid waste
-Pure uranium dust contamination
-Insufficient PPM

## Slide 18: Tailing ponds
-3 ponds up to 10 sq km
-Primarily uranium in H2SO4
-Layered by plastic and clay
-Layers rupture,
contaminating ground water
-Numerous breaches in pipe

## Slide 19: Low grade ore
-Very large volumes
-Lying in the open
-Large dust spread area
-Mostly unmarked
-Stolen for construction

## Slide 20: Coal power station
-500 MW station
-Relis on local coal
-Coal found to contain U2
-Scrubbers should remove it
-Scrubbers often not working

## Slide 21: Worker safety

## Slide 22: Worker safety
The mine management is legally obliged to provide:
-Personal protection equipment (respirators, gloves, head cover) for each shift
-Pprotective clothing for each shift laundered by the Combine after each use;
-Constant water spraying of areas with a large volume of uranium dust (inside mines, open pits, at the ore storage yards, inside the mill complex);
-Constant ventilation of mines and open pits

## Slide 23: Worker safety
-Protective gear is often not issued for extended periods due to shortages.
-A number of mine workers informed us that respirators were often not issued for months at a time, and that even when they were issued, their number was kept down to 1-2 per shift.
-Over the 5 days of working in the area, I do not remember seeing a single respirator on the face of a driver of uranium transporting trucks, a job associated with constant dust exposure.

## Slide 24: Worker safety
-At the chemical processing plant we observed workers working in direct contact with raw uranium ore without gloves, protective hats and respirators.
-Protective clothing is often not issued. Some miners have told us that they have been wearing their personal work clothing and footwear for years, taking it home and washing it themselves.
-We did not observe any water spraying either in the open pit or at the uranium ore storage yard, although the air in both areas is permanently full of uranium dust
-Ventilation of the underground mines seemed to be adequate. However, the turbines in the open pit were standing still during our visit, and it is not clear how regularly they are turned on.

## Slide 25: Worker safety
Combine management is legally obliged to provide:
-Gamma and radon level measurements taken regularly at sites of high risk with the goal of maintaining exposure for workers at levels below permitted maximum;
-Regular health checks (performed by an independent service);
-Regular inspections to ensure that these rules are adhered to.

## Slide 26: Worker safety
-Radiation level is measured regularly, reportedly once a week, at every workstation. However, the workers are not informed about the results of these measurements. Nor can any of them remember a single case of a worker being transferred to a different workstation due to having received excessive doses of radiation.
-Workers employed in areas with a risk for radiation exposure undergo an annual health check. According to the workers, however, these checks are often cursory and superficial, limited to asking how the worker is feeling.
-Blood and urine samples are taken, the workers are never informed about the result of the analyses. In general, all of the workers we spoke with had very low trust in the medical authorities responsible for these checks.

## Slide 27: Worker safety
-The monitoring of application of these safety rules is performed by two bodies: Sanitary Epidemiological Service, and Combine's environmental service.
-The SES checks every work place once every 3 months. They admit that the frequency is insufficient, but due to shortage of personnel and the large size of the Combine an increase in frequency is impossible.
-The chief physician of SES admitted that certain violations, especially violations of personal safety equipment use was very wide spread.

## Slide 28
-The Combine's environmental service has staff permanently attached to each sectiont of the combine. However, their effectiveness is questionable.
-For example -- the head of the environmental service informed us that violations of safety regulations are "extremely rare". Our own observation determined that the number of workers working without respirators (which he admitted constituted a violation) is very high.

## Slide 29: Oktyabrskiy

## Slide 30: Oktyabrskiy
-A village with a population of 3 400.
-Most of the village population consists of mine workers and other Combine employees.
-Village has a kindergarten, a school and an infirmary.
-Mostly small wooden 1 family houses
-Food produced locally

## Slide 31: Oktyabrskiy
-Surrounded by mine entrances, piles of ore, ventilation shafts.
-Ventilation forces mine air through cracks into houses
-On top of underground mine passages
-Dust from ore piles
-Frozen dust from tailing ponds
-Water flows from mines

## Slide 32: Oktyabrskiy
-Radon levels in wells and underground food storages measured to 77 500 bq/cu.m., with the average of 6000 bq/ cu.m.
-Maximum permitted levels in new housing is 100 bq/cu. m.
-Aerial gamma spectronomic analysis determined that the average uranium content in the soil exceeds the background by as much as 20 times.
-In 400 of the village's 1099 households the levels of radon are such that given an average exposure of 20 hour per day, the dosages exceed the maximal limits permitted for professional exposure.

## Slide 33: Further info:
Trip report: https://www.greenpeace.org/static/planet4-sweden-stateless/2023/09/98a1bea6-report-on-the-greenpeace-visit-to-the-priargunskiy-mountain-chemical-.pdf
Video (unedited clip reel):
https://media.greenpeace.org/Detail/27MDHUHA18N3
https://media.greenpeace.org/Detail/27MDHUHA13X0
Thank you!